## Slide 1: Lab 1: Simulator

## Slide 2: Objective
To get familiar with a logic simulator
To develop understanding of how logic gates work

## Slide 3: Getting Started
Download this file (Lab1.pptx) from Blackboard
Open a web browser and go to www.circuitverse.org
  Click “Launch Simulator”

## Slide 4: Lab 1-1
Put an OrGate
Change its BitWidth to 8
Put two Inputs
Change their BitWidth to 8
Connect them to the input ports of the OrGate
Put an Output
Change its BitWidth to 8
Connect it to the output port of the OrGate
Change the Inputs and observe how the Output changes

## Slide 5: Lab 1-2
Put a Multiplexer
Change it BitWidth to 4
Change its Control Signal Size to 2
Put 4 ConstantVals
Change their BitWidth to 4
Change their value to whatever you want
Connect them to input ports of the Multiplexer
Place an Input
Change its BitWidth to 2
Connect it to the Control Signal port of the Multiplexer
Place a HexDisplay
Connect it to the output port of the Multiplexer
Change the Input and observe what is displayed at the Multiplexer

## Slide 6: Lab 1-3
Implement a half adder
Circuit  New Circuit +  “HalfAdder”
A | B | C | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 7: Lab 1-4
Implement a full adder
Circuit  New Circuit +  “FullAdder”
Insert SubCircuit  Select “HalfAdder”

## Slide 8: Lab Assignment
Build a 4-bit full adder
Save your design (login is required) and submit the HTML code.
Project  Save Online  </>Embed  Submit to Blackboard