## Slide 1: Lab 10: FSM Modeling in Verilog

## Slide 2: Objective
To develop understanding of how to model finite state machine in Verilog.

## Slide 3: Getting Started
Download this file (Lab10.pptx) from Blackboard
Open a web browser and go to www.edaplayground.com
Login with your account

## Slide 4: Lab Assignment
Write a SystemVerilog module that Implements a finite state machine that detects an input pattern, 1011
It has three inputs, clk, reset, and in and an one-bit output out.
If the sequence of in is 1011, out becomes 1, otherwise 0.
Two consecutive sequences may overlap.
For example, if the input sequence is 1011011, the output sequence is 0001001.
Use the testbench given in the next slide.
Submit the link of your design.

## Slide 5: Lab Assignment – Testbench
Copy and paste the following code to the left top window (testbench.sv)
module testbench();
logic clk, reset, in;
logic out;
// instantiate device under test
pattern dut(clk, reset, in, out);
always // no sensitivity list, so it always executes
begin
clk = 1; #5; clk = 0; #5;
end
initial begin
$dumpfile("dump.vcd"); $dumpvars;
in = 0; reset = 1; #21; reset = 0; #10
in = 1; #10
in = 0; #10
in = 1; #10
in = 1; #10
in = 0; #10
in = 1; #10
in = 1; #10
in = 1; #10
in = 1; #10
in = 0; #10
in = 1; #10
in = 1; #10
$stop;
end
endmodule

## Slide 6: Expected Result