## Slide 1: Lab 3: Combinational Logic Design

## Slide 2: Objective
To develop understanding of how to design a combinational logic circuit from verbal description

## Slide 3: Getting Started
Download this file (Lab3.pptx) from Blackboard
Open a web browser and go to www.circuitverse.org
  Click “Launch Simulator”

## Slide 4: Lab 3-1
Design a logic that generates 1 if the given 4-bit unsigned integer is greater than 9. (A[3:0] > 10012)
A3 | A2 | A1 | A0 | Y
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
A3 | A2 | A1 | A0 | Y
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 5: Lab Assignment
Design a binary encoded decimal (BCD) converter that translates a 4-bit unsigned binary integer A[3:0] to a 5-bit BCD integer Y[4:0].
When A is interpreted as a decimal number, Y[4] indicates its 10’s digit and Y[3:0] indicates its 1’s digit.
You may use any components available in the simulator.
Submit the HTML code of your design (“</>Embed”).
Examples:
A | Y
0101 | 0 0101
1000 | 0 1000
1010 | 1 0000
1111 | 1 0101