## Slide 1: Lab 5: Sequential Logic Design

## Slide 2: Objective
To develop understanding of how sequential logic works.

## Slide 3: Getting Started
Download this file (Lab5.pptx) from Blackboard
Open a web browser and go to www.circuitverse.org
  Click “Launch Simulator”

## Slide 4: Lab 5-1
Put DflipFlop
Change its BitWidth to 4
Put Adder
Change its BitWidth to 4
Put Input
Change its BitWidth to 4
Put HexDisplay
Put Clock
Connect Clock to Clock of DflipFlop
Connect Q of DflipFlop to A of Adder
Connect Input to B of Adder
Connect Sum of Adder to HexDisplay
Connect Sum of Adder to D of DflipFlop

## Slide 5: Lab Assignment
Design a 4-bit Parallel In Serial Out (PISO) shift register.
It has one 1-bit output: Q.
It has four inputs: CLK, RESET, D[3:0], and L.
  CLK is the clock.
  When RESET=1, the output should become 0.
  If L=1, D is stored to the shift register.
  The output Q is the most significant bit of the shift register.
  If L=0, the bits in the shift register shift to the upper place. The least significant bit is padded with 0.
Examples are given at the following slide.
Submit the HTML code of your design (“</>Embed”).

## Slide 6: Example
L | D | Register | Q
1 | 1011 | 1011 | 1
0 |  | 0110 | 0
0 |  | 1100 | 1
0 |  | 1000 | 1
1 | 0101 | 0101 | 0
0 |  | 1010 | 1
1 | 0010 | 0010 | 0
0 |  | 0100 | 0