## Slide 1: Lab 8: Verilog and Synthesis

## Slide 2: Objective
To develop understanding of how to simulate and synthesis Verilog code.

## Slide 3: Getting Started
Download this file (Lab8.pptx) from Blackboard
Open a web browser and go to www.edaplayground.com
Register for a full account with your KU email account

## Slide 4: Lab 8-1
Copy and paste the following code to the left top window (testbench.sv)
module testbench8();
logic a, b, c;
logic y;
// instantiate device under test
testfunction dut(a, b, c, y);
// apply inputs one at a time
initial begin
$dumpfile("dump.vcd"); $dumpvars;
a = 0; b = 0; c = 0; #10;
c = 1; #10;
b = 1; c = 0; #10;
c = 1; #10;
a = 1; b = 0; c = 0; #10;
c = 1; #10;
b = 1; c = 0; #10;
c = 1; #10;
end
endmodule

## Slide 5: Lab 8-1 – cont’d
Copy and paste the following code to the right top window (design.sv)
module testfunction(input a, b, c,
output y);
assign y = ~b & ~c | a & ~b;
endmodule

## Slide 6: Lab 8-1 – cont’d
Select “Synopsys VCS 2020.03” in Tools & Simulators
Check “Open EPWave after run”
Click “Run”
Select “Yosys 0.9.0” in Tools & Simulators
Check “Show diagram after run”
Click “Run”

## Slide 7: Lab Assignment
Implement the schematic on the right with Verilog.
The inputs are a, b, c and d, and the output is y.
The module name is assignment8.
Use the testbench given in the next slide.
Save and submit the link of your design to the Blackboard.
  Click in the bottom window to copy the URL of your design.

## Slide 8: Lab Assignment – cont’d
Copy and paste the following code to the left top window (testbench.sv)
module testbench();
logic a, b, c, d;
logic y;
// instantiate device under test
assignment8 dut(a, b, c, d, y);
// apply inputs one at a time
initial begin
$dumpfile("dump.vcd"); $dumpvars;
a = 0; b = 0; c = 0; d = 0; #10;
a = 0; b = 0; c = 0; d = 1; #10;
a = 0; b = 0; c = 1; d = 0; #10;
a = 0; b = 0; c = 1; d = 1; #10;
a = 0; b = 1; c = 0; d = 0; #10;
a = 0; b = 1; c = 0; d = 1; #10;
a = 0; b = 1; c = 1; d = 0; #10;
a = 0; b = 1; c = 1; d = 1; #10;
a = 1; b = 0; c = 0; d = 0; #10;
a = 1; b = 0; c = 0; d = 1; #10;
a = 1; b = 0; c = 1; d = 0; #10;
a = 1; b = 0; c = 1; d = 1; #10;
a = 1; b = 1; c = 0; d = 0; #10;
a = 1; b = 1; c = 0; d = 1; #10;
a = 1; b = 1; c = 1; d = 0; #10;
a = 1; b = 1; c = 1; d = 1; #10;
end
endmodule

## Slide 9: Expected Result