## Slide 1: Lab 9: Combinational Logic Design with Verilog

## Slide 2: Objective
To develop understanding of how to model combinational circuit in Verilog using always.

## Slide 3: Getting Started
Download this file (Lab9.pptx) from Blackboard
Open a web browser and go to www.edaplayground.com
Login with your account

## Slide 4: Lab 9-1
Copy and paste the following code to the left top window (testbench.sv)
module testbench9();
logic [3:0] in;
logic [1:0] out;
// instantiate device under test
priority_casez dut(in, out);
initial begin
$dumpfile("dump.vcd"); $dumpvars;
in = 4'b1101; #20;
in = 4'b0111; #20;
in = 4'b0010; #20;
in = 4'b0001; #20;
in = 4'b0000; #20;
end
endmodule

## Slide 5: Lab 9-1 – cont’d
Copy and paste the following code to the right top window (design.sv)
module priority_casez(input [3:0] a,
output reg [1:0] y);
always @(a)
casez(a)
4'b1???: y = 2'b11; // ? = don’t care
4'b01??: y = 2'b10;
4'b001?: y = 2'b01;
4'b0001: y = 2'b00;
default: y = 2'b00;
endcase
endmodule

## Slide 6: Lab 9-1 – cont’d
Select “Synopsys VCS 2020.03” in Tools & Simulators
Check “Open EPWave after run”
Click “Run”
Select “Yosys 0.9.0” in Tools & Simulators
Check “Show diagram after run”
Click “Run”

## Slide 7: Lab Assignment
Write a SystemVerilog module of a 2-input thermometer code adder.
An M-bit thermometer code for the number k consists of k 1’s in the least significant bit positions and (M-k) 0’s in all the more significant bit positions.
The two inputs are 3-bit long and the output is 6-bit long.
Assume the inputs are always encoded correctly as thermometer code.
The output should also be in thermometer code.
Examples
  000 + 000 = 000000
  111 + 011 = 011111
  111 + 111 = 111111
  011 + 001 = 000111
Copy and paste the testbench code in the next slide to the left top window (testbench.sv).
Submit the link of your design.

## Slide 8: Lab Assignment – Testbench
module testbench9();
logic [2:0] a;
logic [2:0] b;
logic [5:0] y;
// instantiate device under test
thermaladd dut(a, b, y);
// apply inputs one at a time
initial begin
$dumpfile("dump.vcd"); $dumpvars;
a = 3'b000; b = 3'b000; #10;
a = 3'b111; b = 3'b011; #10;
a = 3'b111; b = 3'b111; #10;
a = 3'b011; b = 3'b001; #10;
a = 3'b000; b = 3'b000; #10;
#10;
end
endmodule

## Slide 9: Expected Result